## Slide 1: Respirators and other equipment
Marcelina Szołucha 7466 Magdalena Matusiak 7388

## Slide 2: Respirator what is it ?
A ventilator is a device that assists the lungs. It can be a life-saving machine if you suffer from a medical condition that makes it difficult to breathe properly or if you cannot breathe on your own at all.
A ventilator helps force air in and out of the lungs so the body can get the oxygen it needs. A person who needs a ventilator may wear a fitted mask, which helps oxygen from the ventilator reach the lungs, or, if their condition is more serious, a breathing tube, which is inserted into the throat to supply the lungs with oxygen.
Respirators are most commonly used in hospital settings. The doctor will control the amount of oxygen injected into the lungs by the ventilator. Another name for a ventilator is an "artificial lung."

## Slide 3: How does the respirator work?
In its simplest form, a modern ventilator consists of a compressed air tank or turbine, air and oxygen sources, a set of valves and tubing, and a disposable or reusable "patient circuit." The air tank is pneumatically compressed several times a minute to deliver room air or, in most cases, an air/oxygen mixture to the patient. If a turbine is used, it pushes air through a ventilator equipped with a flow valve that regulates pressure to meet patient-specific parameters. Once the pressure is released, the patient will exhale passively due to the elasticity of the lungs, and the exhaled air is usually released through a one-way valve in the patient's circuit called the patient manifold.

## Slide 4
Respirators can also be equipped with monitoring and alarm systems for patient-related parameters (e.g., pressure, volume and flow) and ventilator functions (e.g., air leakage, power failure, mechanical failure), emergency power supply, oxygen tanks and remote control . The pneumatic system is now often replaced by a computer-controlled turbopump.

## Slide 5
Modern ventilators are electronically controlled by a small built-in system that allows the pressure and flow characteristics to be fine-tuned to the individual patient's needs. Fine-tuned ventilator settings also serve to make ventilation more bearable and comfortable for the patient. Depending on the type of ventilation needed, the end of the patient circuit can be non-invasive (mask) or invasive (tube).

## Slide 6: Respirator with face mask
The use of a face mask to deliver oxygen to the lungs is known as non-invasive ventilation.
With this type of ventilation, a fitted plastic mask is placed over the nose and mouth. A tube will be connected to the mask to force air into the lungs. This method is usually used in cases where breathing problems are less severe.

## Slide 7
This method has several advantages.
It is more convenient than using a tube that goes down the throat;
It does not require sedation;
It allows you to speak, swallow and cough;
It can lower the risk of side effects and complications, such as infection and pneumonia, which are more common with endotracheal tube ventilation.

## Slide 8: Respirator with endotracheal tube
In more severe cases, the patient will need an endotracheal tube placed in the throat and trachea. This is called invasive ventilation. Usually, the patient will be sedated before this procedure is performed, as it can cause pain and discomfort.
The endotracheal tube and ventilator perform different tasks. The ventilator forces a mixture of air and oxygen into the patient's lungs to deliver oxygen to the body. The ventilator can also maintain a constant low pressure, called positive end expiratory pressure (PEEP), to prevent air bubbles from collapsing in the lungs. An endotracheal tube allows doctors and nurses to suction mucus from the trachea.

## Slide 9
The endotracheal tube and ventilator perform different tasks. The ventilator forces a mixture of air and oxygen into the patient's lungs to deliver oxygen to the body. The ventilator can also maintain a constant low pressure, called positive end expiratory pressure (PEEP), to prevent air bubbles from collapsing in the lungs. An endotracheal tube allows doctors and nurses to suction mucus from the trachea.

## Slide 10
If a patient is diagnosed with a tracheal obstruction, for example due to a tumor, or needs a ventilator for a long time, he or she may need a tracheostomy procedure. During a tracheostomy, a surgeon makes an opening in the patient's neck and trachea, and then inserts a breathing tube called a tracheostomy tube into the opening. The tracheostomy tube is then connected to a ventilator. The tracheostomy tube can stay in the patient's body for as long as needed, but it does not have to be there permanently and can be removed if the patient no longer needs it. The tracheostomy tube can be used to talk and eat.

## Slide 11: Respirators - types
Types of respirators include the following.
Stationary respirators - found in many variants. Depending on the model and manufacturer, they are characterized by various additional features. They are used in hospital wards.
Ambulance/transport ventilators - their characteristic feature is their high shock resistance and size, as they are much smaller to their stationary counterparts. That's not all, however, as these ventilators are also designed to operate in harsh environments (they are water and frost resistant). They support a patient's breathing even while they are being transported to the hospital by ambulance or rescue helicopter.

## Slide 12
Neonatal ventilators - designed specifically for newborns, operate in a mode suitable for ventilating the youngest patients. What's more, they also fit most types of incubators. They are among several devices found in neonatal pathology and intensive care units.

## Slide 13: Respirator - modes of operation
Respirators can operate under various modes of operation, among which are:
SIMV (synchronized intermittent mandatory ventilation) respiration - guarantees a certain number of breaths, but the patient's breaths are partly their own, reducing the risk of hyperinflation or alkalosis. Forced breaths are synchronized with spontaneous breaths. The disadvantages of SIMV are increased work of breathing and a tendency to decrease cardiac output, which can prolong ventilator dependence. Adding pressure support to spontaneous breaths can reduce some of the work of breathing. SIMV has been shown to reduce cardiac output in patients with left ventricular dysfunction.

## Slide 14
PSV (pressure support ventilation) respiration - allows the patient to determine the filling volume and respiratory rate, so it can only be used to support spontaneous breathing. Pressure support can be used to overcome the resistance of the ventilator tubing in the next cycle or to support spontaneous breathing. This mode is used with specialized face masks.

## Slide 15
PCIRV (pressure-controlled inverse ratio ventilation; pressure-controlled inverse I:E ratio ventilation) - a pressure-controlled ventilation mode in which most of the time is spent at a higher (inspiratory) pressure. Early studies were promising, but the risk of auto PEEP and hemodynamic deterioration due to shortened expiratory time and increased mean airway pressure generally outweighs the small potential for improved oxygenation.

## Slide 16
APRV ventilation (airway pressure release ventilation) - is a variation of CPAP (continuous positive airway pressure; respiratory support with continuous positive pressure), which temporarily releases pressure during exhalation. This unique mode of ventilation results in higher average airway pressure. Patients are able to spontaneously ventilate at both low and high pressures, although usually most (or all) of the ventilation occurs at high pressure. In the absence of breath attempts, APRV and PCIRV are identical. As in PCIRV, the hemodynamic problem is an issue in APRV. In addition, APRV usually requires increased sedation.

## Slide 17
PEEP (positive end expiratory pressure; positive end expiratory pressure ventilation) ventilation - a method of ventilation in which airway pressure is maintained above atmospheric pressure at the end of expiration by means of a mechanical impedance, usually a valve, in the circuit. The goal of PEEP is to increase the volume of gas remaining in the lungs at the end of expiration to reduce lung blood flow and improve gas exchange. PEEP is performed in ARDS (acute respiratory distress syndrome) to allow a reduction in the level of oxygen administered.

## Slide 18
CPAP (continuous positive airway pressure; continuous positive pressure assisted breathing) ventilation - is a form of positive airway pressure (PAP) ventilation in which a constant level of pressure, greater than atmospheric pressure, is continuously applied to a person's upper airway. The use of positive pressure can be aimed at preventing upper airway collapse, which occurs in obstructive sleep apnea, or reducing work of breathing in conditions such as acute uncompensated heart failure. CPAP therapy is very effective in treating obstructive sleep apnea.

## Slide 19
CMV (continuous mandatory ventilation), continuous mandatory ventilation - in this mode, each breath is taken by the ventilator for the patient. The patient also has the option of taking additional breaths. These must have the parameters indicated by the ventilator.
AMV (assisted mechanical ventilation) respiration, assisted mechanical ventilation - this mode is based on the positive respiratory pressure generated.

## Slide 20
IMV (Intermittent mandatory ventilation), intermittent mandatory ventilation - this mode is usually used for premature babies and newborns. The principle of operation is that the ventilator performs part of the respirations, and between the mechanical action of the ventilator, the newborn can also breathe independently. However, it is very important that there is no conflict between self-breathing and the breaths performed by the ventilator.

## Slide 21: Indications for the use of a ventilator
The inability to breathe properly on its own is known as respiratory failure and is a life-threatening condition.
If the brain, heart, liver, kidneys and other organs do not receive enough oxygen, they will not be able to function as they should. A ventilator can help the organs get the oxygen they need to function.

## Slide 22: How long should one be connected to a ventilator?
A ventilator can save lives, but its use comes with risks. It does not solve the problem that led the person to need a ventilator; it simply helps the patient until other therapies become effective or the patient recovers on his or her own. Doctors always try to help patients disconnect from the ventilator as early as possible.

## Slide 23
"Weaning" refers to the process of disconnecting a patient from a ventilator. Some patients may only be on a ventilator for a few hours or days, while others may require a ventilator for longer. How long a patient needs to be connected to a ventilator depends on a number of factors. These may include overall strength, the condition of the lungs before the ventilator is turned on, and the number of other organs (such as the brain, heart and kidneys) involved. Some people's condition will never improve enough for them to be disconnected from the ventilator.

## Slide 24: Respirator vs. patient condition monitoring
Most patients connected to a ventilator are monitored in the intensive care unit. Anyone on a ventilator in the intensive care unit will be connected to a monitor that measures heart rate, respiratory rate, blood pressure and oxygen saturation ("sat O2"). Other tests that may be performed include a chest x-ray and a blood draw to measure oxygen and carbon dioxide ("blood gases").
Members of the healthcare team (including doctors, nurses) will use this information to assess the patient's condition and make adjustments to the ventilator if necessary.

## Slide 25: Risks associated with connection to a ventilator
A ventilator can save our lives. However, like other treatments, it can cause potential side effects. This is more common if we use a respirator for a long time.
Some of the most common risks associated with being under a respirator include the following problems and ailments.

## Slide 26
Infection. This is one of the main risks associated with being on a ventilator with an endotracheal tube. The accumulation of fluids and mucus in the throat and trachea can allow germs to accumulate in the respiratory tract. These germs can then enter our lungs. This can increase the risk of developing pneumonia. Sinus infections are also common with an endotracheal tube. We may need antibiotics to treat pneumonia or sinus infections.
Irritation. The respiratory tract can rub and irritate the throat or lungs. It can also make it difficult to cough, which helps rid the lungs of dust particles and irritants.

## Slide 27
Vocal cord problems. The endotracheal tube passes through the larynx, where the vocal cords are located, which is the reason why you can't speak when using a ventilator. The endotracheal tube can damage the larynx.

## Slide 28
Collapsed lung (pneumothorax). Sometimes part of the lung can be weakened, leading to a hole, allowing air to leak out and causing the lung to collapse. If the lung collapse is severe enough, it can cause death. To re-expand the lung, a tube should be placed in the chest to drain the leaking air. Once the lung has healed, the tube can be removed.
Clots. Lying in the same position for long periods of time can increase the risk of blood clots.

## Slide 29
Side effects of medications. Sedatives and painkillers can make a patient appear confused or delirious (side effects may continue to affect the patient after the drugs are discontinued). The health care team tries to adjust the right amount of medication for the individual. Different people will react differently to each medication. If a drug is needed to prevent muscle movement, muscles may be weak for a while after the drug is discontinued. This may improve over time. Unfortunately, in some cases, muscle weakness persists for weeks to months.

## Slide 30
Nerve and muscle damage. Lying motionless for days, using sedatives and not breathing on your own can result in nerve and muscle disorders.
Fluid retention. Can be caused by continuous infusions, drug toxicity and kidney failure.

## Slide 31
Lung damage. The pressure of air introduced into the lungs via a ventilator can damage the lungs. Doctors try to minimize this risk by using the least amount of pressure needed. Very high levels of oxygen can also be harmful to the lungs. Doctors give only as much oxygen as needed to make sure the body gets enough to supply vital organs. Sometimes it is difficult to reduce this risk when the lungs are damaged. However, this damage can improve if a person is able to recover from a serious illness.

## Slide 32
Inability to be disconnected to a ventilator. Sometimes the disease that caused the patient to need a ventilator does not go away despite treatment. When this happens, the health care team will discuss treatment issues with continued use of the ventilator. Often, the health care team will have these discussions with family members or the patient, if the patient is able to participate. In situations where the patient is not recovering or is deteriorating, a decision may be made to stop using the ventilator and allow the patient to die.

## Slide 33: Mammal what is it?
A medical suction machine is an indispensable device in modern healthcare, used for effective suction of biological fluids and tissue debris, such as blood, pus or respiratory secretions. Its operation is based on a vacuum mechanism, which effectively sucks unwanted substances out of the patient's body by means of a pressure difference. Suction machines are widely used both in the hospital environment during surgical procedures and in home care - especially for intubated patients, those suffering from cystic fibrosis, those who have difficulty expectorating phlegm on their own or those using ventilators.

## Slide 34
This device is crucial for maintaining airway patency and providing comfort to patients requiring intensive care. Its simple yet effective operating principle makes the medical suction machine an indispensable helper in many medical scenarios, helping to improve the quality of care and patient safety.
Various types of medical suction units are available on the market to meet the diverse needs of patients and healthcare professionals.

## Slide 35
Among them are:
Stationary electric suction machines: Powered directly from the mains, they are highly efficient and have a spare tank for extracted fluids. They are indispensable in operating rooms, treatment rooms and in home care of patients.
Portable rechargeable suction units: they do not require a permanent connection to a power source and are ideal for use in ambulances and when transporting patients, providing support in all conditions.
Handheld suction units: lightweight and easy to use, they are preferred by emergency medical teams during rescue operations.

## Slide 36
It is worth noting that medical suction machines are not only used to remove fluids, but sometimes also gases and tissues. These devices must be reliable, durable, easy to clean, equipped with antibacterial filters and overfill protection. They make possible the daily work of doctors performing simple procedures as well as complex surgeries.

## Slide 37: Components of the suction system
Vacuum regulator: This item allows you to control the regulation of vacuum. It allows the surgeon to adjust the suction force according to the type of fluids, such as blood, lymph or secretions. The regulator ensures a dry surgical environment, which is essential for a good view of the patient's tissues and vessels.
Collection container: This is the place where collected secretions go. Modern mammals have systems to prevent overflow of the reservoirs, which is important for maintaining septic conditions during surgery.

## Slide 38
Vacuum suction machines: They are used to suction body fluids, tissues and gases. With them, the surgeon works in a dry environment and secretions do not back up into the surgical area. High-quality suction machines have special antibacterial filters and easily sterilizable reservoirs.
Injector suction: In places where there is no access to a central vacuum system, injector suction devices are used. They work by the Venturi effect, creating a pressure differential between the liquid and the discharge chamber. They can be stand-alone units or part of an integrated system.

## Slide 39
Vacuum regeneration pump. As a rule, central in the hospital. The yellow tubing system in the operating room is built so that it can't be short-circuited with a connector for any of the anesthetic gases. This suction system is connected to the main tank by a system of antimicrobial filters and a vacuum pump.
A reservoir in the operating room that collects aspirated fluids. The tank system includes a filter with a valve float mechanism to prevent the pump from being flooded by the aspirated fluid.
The tubing system connecting the reservoir to the suction catheter is soft or rigid (Yankauer). Tracheal suctioning should not be unduly prolonged, as this can cause lung drops and bradycardia.

## Slide 40
Thank you for your attention 